## Slide 1
Designing with 802.15.4 and ZigBee
Industrial Wireless Applications Summit
San Diego, California
9 March 2004
Jon Adams
Director, Radio Technology and Strategy
Motorola Wireless and Mobile Systems Group
Tempe, Arizona
jta@motorola.com
+1 480.413.3439 Office
Chairman
ZigBee Qualification Group
ZigBee Alliance

## Slide 2: IEEE 802.15.4 Basics
802.15.4 is a simple packet data protocol for lightweight wireless networks
  Channel Access is via Carrier Sense Multiple Access with collision avoidance and optional time slotting
  Message acknowledgement and an optional beacon structure
  Multi-level security
  Three bands, 27 channels specified
    2.4 GHz: 16 channels, 250 kbps
    868.3 MHz : 1 channel, 20 kbps
    902-928 MHz: 10 channels, 40 kbps
  Works well for
    Long battery life, selectable latency for controllers, sensors, remote monitoring and portable electronics
  Configured for maximum battery life, has the potential to last as long as the shelf life of most batteries

## Slide 3: PHY Performance
802.15.4 has excellent performance in low SNR environments
Bluetooth

## Slide 4: IEEE 802.15.4 MAC Overview
Employs 64-bit IEEE & 16-bit short addresses
  Ultimate network size can reach 264 nodes (more than we’ll probably need…)
  Using local addressing, simple networks of more than 65,000 (2^16) nodes can be configured, with reduced address overhead
Three devices specified
  Network Coordinator
  Full Function Device (FFD)
  Reduced Function Device (RFD)
Simple frame structure
Reliable delivery of data
Association/disassociation
AES-128 security
CSMA-CA channel access
Optional superframe structure with beacons
Optional GTS mechanism

## Slide 5: Data Frame format
One of two most basic and important structures in 15.4
Provides up to 104 byte data payload capacity
Data sequence numbering to ensure that packets are tracked
Robust structure improves reception in difficult conditions
Frame Check Sequence (FCS) validates error-free data
Notes: <number>
<footer>
<header>
<date/time>
Frame control: + type of frame (4 types), format of address field, controls Ack, I.e. specifies how the frame looks and what it contains. The ACK and MAC command are lower level used for peer-to-peer
Sequence number: and Frame check sequency: verifies the integrity of the MAC frame. A transmission is considered successful if the ack frame contains the same sequence number as the previous frame. FCS is a 16-bit cyclic redundancy check (CRC)
Address field size: can contain both source and destination info

## Slide 6: Acknowledgement Frame Format
The other most important structure for 15.4
Provides active feedback from receiver to sender that packet was received without error
Short packet that takes advantage of standards-specified “quiet time” immediately after data packet transmission
Notes: <number>
<footer>
<header>
<date/time>
Frame control: + type of frame (4 types), format of address field, controls Ack, I.e. specifies how the frame looks and what it contains. The ACK and MAC command are lower level used for peer-to-peer
Sequence number: and Frame check sequency: verifies the integrity of the MAC frame. A transmission is considered successful if the ack frame contains the same sequence number as the previous frame. FCS is a 16-bit cyclic redundancy check (CRC)
Address field size: can contain both source and destination info

## Slide 7: MAC Command Frame format
Mechanism for remote control/configuration of client nodes
Allows a centralized network manager to configure individual clients no matter how large the network
Notes: <number>
<footer>
<header>
<date/time>
Frame control: + type of frame (4 types), format of address field, controls Ack, I.e. specifies how the frame looks and what it contains. The ACK and MAC command are lower level used for peer-to-peer
Sequence number: and Frame check sequency: verifies the integrity of the MAC frame. A transmission is considered successful if the ack frame contains the same sequence number as the previous frame. FCS is a 16-bit cyclic redundancy check (CRC)
Address field size: can contain both source and destination info

## Slide 8: Beacon Frame format
Beacons add a new level of functionality to a network
Client devices can wake up only when a beacon is to be broadcast, listen for their address, and if not heard, return to sleep
Beacons are important for mesh and cluster tree networks to keep all of the nodes synchronized without requiring nodes to consume precious battery energy listening for long periods of time
Notes: <number>
<footer>
<header>
<date/time>
Frame control: + type of frame (4 types), format of address field, controls Ack, I.e. specifies how the frame looks and what it contains. The ACK and MAC command are lower level used for peer-to-peer
Sequence number: and Frame check sequency: verifies the integrity of the MAC frame. A transmission is considered successful if the ack frame contains the same sequence number as the previous frame. FCS is a 16-bit cyclic redundancy check (CRC)
Address field size: can contain both source and destination info

## Slide 9: ZigBee is Mesh Networking
ZigBee End Device (RFD or FFD)
ZigBee Router (FFD)
ZigBee Coordinator (FFD)
Mesh Link
Star Link

## Slide 10: Motorola 802.15.4 / ZigBee™ solution
Features
  2.4 GHz Band, -92 dBm RX sensitivity at 1% PER
    IEEE requirement is at least –85 dBm
  Power supply 2.0-3.6 V w/ on-chip regulator, logic interface 1.7 to 3.3
    Runs off a single Li or 2 alkaline cells
  Complete RF transceiver data modem – antenna in, fully packetized data out
  Data and control interface via standard SPI at 4 MHz minimum
  802.15.4 MAC supplied
  Four new Motorola HCS08 MCUs will interoperate with the data modem chip
    Often 802.15.4 functionality can be added to existing systems simply by including the modem chip and reprogramming an existing MCU that may already be in the application
  HC08 RAM/FLASH configurations from 384B/4kB to 2kB/60kB depending upon application SW needs

## Slide 11: System Simplicity and Flexibility
Motorola RF Packet Radio
Motorola 8-Bit MCU

## Slide 12: Motorola’s 802.15.4 Platform Advantages
One-Stop-Shop Solution
  Single source for platform solution
    Integrated Circuits, Reference Designs, Modules, Stack Software, Development Systems
Key technology enhancements provide for a superior solution
  Excellent adjacent channel rejection
    No external filtering required under most conditions
  High Sensitivity Radio Solution
    7 dBm better than spec – longer range
  Extended Temperature Operating Range
    -40°C to +85°C for industrial and automotive applications
  Operating voltage range optimized for alkaline or lithium primary cells
    2.0 Vdc to 3.6 Vdc, disposable
      Nearly 100% of available battery life whether Alkaline or Lithium
      Normal 2.7v EOL silicon systems can only get perhaps 30% of available alkaline battery energy
  Adjustable TX Output power
    Improved coexistence for short range applications
IEEE Participation and ZigBee™ Alliance leadership
  Technology and standards driver
  Early access to new technology
Notes: <number>
<footer>
<header>
<date/time>

## Slide 13: 15.4/ZigBee and Bluetooth
Instantaneous Power Consumption
  15.4 Transceivers are “similar” to Bluetooth Transceivers
    802.15.4
      O-QPSK with shaping
      Max data rate 250kbps over the air
      2Mchips/s over the air Direct Sequence Spread Spectrum (62.5ksps*32 spread)
      -92 dBm sensitivity nominal
      40ppm xtal
    Bluetooth
      FSK
      Max data rate 720kbps over the air
      1Msps over the air Frequency Hop Spread Spectrum (79 channels @ 1600 hps)
      -83 to -84 dBm sensitivity nominal
      20ppm xtal
Instantaneous power consumption will be similar for the raw transceivers without protocol
Bluetooth’s FHSS makes it impractical to create extended networks without large synchronization cost

## Slide 14: 15.4 Protocol Built for the Mission
15.4 Protocol was developed for very different reasons than Bluetooth
  802.15.4
    Very low duty cycle, very long primary battery life applications as well as mains-powered
    Static and dynamic mesh, cluster tree and star network structures with potentially a very large number (>>65534) of client units, low latency available as required
    Ability to remain quiescent for long periods of time without communicating to the network
  Bluetooth
    Moderate duty cycle, secondary battery operation where battery lasts about the same as master unit
    Wire replacement for consumer devices that need moderate data rates with very high QoS and very low, guaranteed latency
    Quasi-static star network structure with up to 7 clients (and ability to participate in more than one network simultaneously)
    Generally used in applications where either power is cycled (headsets, cellphones) or mains-powered (printers, car kits)
Protocol differences can lead to tremendous optimizations in power consumption

## Slide 15: Home/Light Commercial Spaces

## Slide 16: Industrial/Commercial Spaces
Warehouses, Fleet management, Factory, Supermarkets, Office complexes
Gas/Water/Electric meter, HVAC
Smoke, CO, H2O detector
Refrigeration case or appliance
Equipment management services & Preventative maintenance
Security services
Lighting control
Assembly line and work flow, Inventory
Materials processing systems (heat, gas flow, cooling, chemical)
Energy, diagnostics, e-Business services
Gateway or Field Service links to sensors & equipment
  Monitored to suggest PM, product updates, status changes
Nodes link to PC for database storage
  PC Modem calls retailer, Service Provider, or Corp headquarters
  Corp headquarters remotely monitors assets, billing, energy management
HVAC
Field Service or mobile worker
Service
Provider
Retailer
Corp
Office
Mfg Flow
Temp.
Sensor
Security
Sensor
Database
Gateway
Telephone
Cable line
Back End
Server
Materials handling

## Slide 17: Peel-n’-Stick Security Sensors
Battery Operation
  2 AA Alkaline or 1 Li-AA cell
802.15.4/ZigBee Mode
  Non-beacon network environment
Sensor process
  RC Oscillator waking up MCU and doing network check-in at some interval
    Many security systems have between ~10 second and ~15 minute requirement
  On a sensor event, device immediately awakens and reports in to network
802.15.4 XCVR
MCU
IRQ
SPI
SPI
16.000MHz
Vcc
Vcc
4
3Vdc
Security
Sensor
OSC1
CLK

## Slide 18: Security Sensor Timing
Battery-Powered Sensor
Mains-Powered Router
Interval timer expires: Wake Up
CCAx2
RX
TX
ACK TX OPT: Pending ON
ACK RX
TX Data
RX Data
Set Interval timer
Sleep
256µs
~650µs
RX>TX
192µs
TX>RX
192µs
~350µs
RX>TX
~650µs
Check-in only ~1640µs
Event and Get Data ~2300µs

## Slide 19: 802.15.4 Security Sensor
Only at 15-min interval does BT reach battery shelf life
Any check-in interval exceeding ~14 sec allows sensor to surpass alkaline battery shelf life

## Slide 20: Body-Worn Medical Sensors
Heartbeat Sensor
  Battery-operated using CR2032 Li-Coin cell
802.15.4/ZigBee Mode
  Network environment using Guaranteed Time Slot (GTS)
  Network beacons occurring either every
    960ms or 61.44s (closest values to 1 and 60 s)
Sensor has two ongoing processes
  Heartbeat time logging
  Transmit heartrate and other information (8 bytes total)
    Instantaneous and average heart rate
    Body temperature and battery voltage
time
heartbeat
GTS
Beacon
802.15.4 XCVR
MCU
32.768kHz
IRQ
SPI
SPI
16.000MHz
Vcc
Vcc
INT
IRQ/
4
OSC1
OSC2
3Vdc
RESET
Heartbeat
Sensor

## Slide 21: 802.15.4/ZigBee vs Bluetooth
Bluetooth 30 days (park mode @ 1.28s)
802.15.4/ZigBee more battery-effective at all beacon intervals greater than 0.246s
At beacon interval ~1s, 15.4/ZigBee battery life 85 days
At beacon interval ~60s, 15.4/ZigBee battery life approx 416 days

## Slide 22: Summary
IEEE 802.15.4 and ZigBee
  Designer concentrates on end application
    Silicon vendors and ZigBee Alliance take care of transceiver, RF channel and protocol
  Reliable and robust communications
  Flexible network architectures
  Very long primary battery life (months to years to decades)
  Very inexpensive Bill Of Materials
  Low system complexity for the OEM
More Information
  Motorola: www.motorola.com/zigbee
  ZigBee: www.zigbee.org